## Slide 1: Constraint Conversion in NX 6/7/7.5
Jim Carrington
Notes: <number>

## Slide 2: Assembly Constraints
New implementation of constraint-based component positioning
Replaces NX 4 “mating conditions”
  Easier to use
  More efficient
  More consistent with sketcher
  First available in NX 5

## Slide 3: Transitioning Mating Conditions → Assembly Constraints
 | NX 5 | NX 6 | NX 7
Methods available (mating/constraints) | Both (user preference) | Both (user preference) | Assembly Constraints only
Constraint conversion tools | Interactive UI in NX | Interactive UI in NX Batch conversion through refile_part | Interactive UI in NX Batch conversion through refile_part
Recommendation for customers with existing mating conditions | Use mating conditions | Use assembly constraints | Use assembly constraints

## Slide 4: Constraint conversion
Benefits of converting constraints
NX 6 provides good support for working in assemblies with mixed constraint types
However, improved user experience if only assembly constraints exist
Mating conditions
Assembly constraints
A
B
C
D
E
OK
Ideal !
A
B
C
D
E

## Slide 5: Constraint conversion
A
B
C
D
E
Benefits of converting constraints
User sees benefits of assembly constraints with every assembly
User only has to understand one constraints system and UI
Dynamic dragging available in all assemblies
  No need to switch UI for older assemblies
Assembly sequencing only recognises one constraint type at a time
Ideal !

## Slide 6: Using refile_part for bulk constraint conversion
Option | Capability
-convert_mcs | Enables constraint conversion during refile & generates conversion report
Additional options (NX 6.0.1): | 
-mc_parts_only | Only refile parts that contain constraints
-mc_dry_run | Convert constraints & generate report without saving any parts
-mc_dont_load_referenced geometry | Do not force load parts containing referenced geometry (conversion not checked)

## Slide 7: Recommended refile process
Re-file parts without converting constraints
Re-file with “dry run” option & check conversion report
Re-file with constraint conversion options
Examine report Check & fix up parts with warnings
-convert_mcs
-mc_parts_only
-mc_dry_run
-convert_mcs
-mc_parts_only
Examine & fix-up any serious problems
Issues
OK

## Slide 8: Conversion checking process
Steps taken by NX during interactive conversion and refile_part:
Solve using mating conditions & remember component positions
Convert constraints
Solve using assembly constraints
Compare new and old component positions
For components that would be moved:
      do not apply reposition
      suppress constraints causing movement
Customer defaults to specify allowable movement
Suppress constraints that cause movement greater than this
Report constraints that cause movement greater than this

## Slide 9: How to investigate a conversion warning or failure
Search conversion report for warnings and errors
For each assembly containing problem constraints:
Load assembly (no components)
Convert constraints interactively
Look for messages in Alerts column to find problem constraints
Isolate problem constraints using Show/Hide Constraints
Investigate & fix problem
(e.g. unsuppress to understand problem)