## Slide 1: Datenexport
Erstellt von:
J.Feuerstein 30.11.2007
Mitschriften zum Datenexport via Tce/Nx mit dem JobManager

## Slide 2: Export Bedingungen
Übersicht welche wie werden die unterschiedlichen Datasettypen exporiert
Datasettype | Step Export | Parasolid Export | DXF Export | JTExport
Einzelteile (SP=Single Parts) |  |  |  | 
UGMASTER/SP | YES | YES | NO | 
UGALTREP/SP | YES | YES | NO | 
UGPART/SP | NO? | NO | YES | 
Baugruppen (AP=Assembly Parts) |  |  |  | 
UGMASTER/AP | YES | YES | NO | 
UGALTREP/Ap | YES | YES | NO | 
UGPART/Ap | NO? | NO | YES | 
Export Optionen:
  Mit welchen Refset Einstellungen soll exportiert werden  siehe load_options.def
  Was ist zu unterscheiden beim Export von SP Single Parts und AP Assembly Parts
  Wie sollen bei den Exports Rohteil und Fertigteil unterschieden werden Frage soll das Rohteil beim Export enthalten sein
  Export von Altreps
  Export DXF ..\dxfdwg_M.def wichtig:  enthält verweis auf
  Export DXF Fonts  ..\dxfdwg_CHARACTERFONT_MAPPING_DataExpo.def ..\dxfdwg_M.def wichtig:  enthält verweis aufdxfdwg_CHARACTERFONT_MAPPING_DataExpo.def

## Slide 3: Einstellungen JobManager
Einstellungen Scripts/Param

## Slide 4: Einstellungen JobManager
Einstellungen Job Control

## Slide 5: Ugto2d.exe DXF Export Optionen für
Optionparameter for Ugto2D
$UGII_BASE_DIR/ugto2d/ugto2d [options]
You can give the options in any order. Each uses an option= format. Use spaces to delimit multiple options.
Valid options include:
[i=]<input part file name> | Mandatory
[o=<output part file name>] | Optional, default: <input part file name>_2d.prt
[l=<log file name>] | Optional, default: <input part file name>_2d.log
[d=<user-defined settings file>] | Optional, default: ugto2d.def
[a=<assembly options file>] | Optional, default: load_options.def
[m=<'output to' mode>] | Optional, default: m (for Modeling) Valid modes are: d (for Drafting) and m (for Modeling)
[draw=<choose drawing to translate>] | Optional, default: current drawing
[view=<choose view to translate>] | Optional, default: current view)
Tce | -pim=yes –u=TceUser –p=TcePasswort
You can run the command line in Teamcenter Engineering on Windows. The following example translates UGMASTER 000201/a into a 2D part file: 000201_a_2d.prt
1. Source your Teamcenter Engineering environment.
2. set PATH=%UGII_ROOT_DIR%;%PATH%
3. ugto2d.exe i=@DB000201/A
Input File Name
The i= label is optional when specifying the input part file name.
If there is no input file name given on the command line, you are asked for input data. See Example of Prompt - Mode Invocation of Translator.
You can supply input file name(s) through the settings file using the INPUT_PARTS_LIST keyword. You can control the input directory using the INPUT_PARTS_DIR keyword.

## Slide 6: Ugto2d Command Line/User-Defined Settings File Examples
Command: ugto2d onedrawing.prt AND ugto2d multidrawing.prt d=my.def
Settings: using all defaults
Yields: onedrawing_2d.prt AND multidrawing_2d.prt
Command: ugto2d twodrawings.prt d=my.def
Settings: DEFAULT_DRAWING_CNV = _ALL_
Yields: _twodrawings_sh1_2d.prt AND twodrawings_sh2_2d.prt
Command: ugto2d d=my.def
Settings:
INPUT_PARTS_DIR=d:\in\
OUTPUT_PARTS_DIR=f:\out\
INPUT_PARTS_LIST=one.prt, twodrawings.prt, three.prt
OUTPUT_PARTS_LIST=bob.prt, fred.prt, three.prt
Reads in: d:\in\one.prt, d:\in\twodrawings.prt, d:\in\three.prt
Writes out: f:\out\bob_2d.prt, f:\out\fred_sht1_2d.prt, f:\out\fred_sht2.prt, f:\out\three_2d.prt
Command: ugto2d multidrawing.prt d=my.def
Settings:
INPUT_PARTS_DIR=/in/
OUTPUT_PARTS_DIR=OUTPUT_TO_INPUT_DIR
DEFAULT_CNV_MODE = DRAFTING
DEFAULT_DRAWING_CNV = CURRENT
ASSEM_OPTIONS=/asm/missingcompok/load_options.def
Reads in: /in/multidrawing.prt
Writes out: /in/multidrawing_2d.prt with results in drafting rather than in modeling. Only the current drawing is processed, rather than processing _ALL_ drawings. The provided options file governs assembly loading behaviors. This could be supplied via the a=/asm/missingcompok/load_options.def command line option.
Command: ugto2d multi.prt d=my.def
Settings:
INPUT_PARTS_DIR=d:\in\
OUTPUT_PARTS_DIR=OUTPUT_TO_CURR_DIR
Reads: d:\in\multi.prt
Writes (given current directory is m:\test\fri\batch\):
m:\test\fri\batch\multi_sh1_2d.prt
m:\test\fri\batch\multi_sh2_2d.prt

## Slide 7: DXF/DWG Translator
Settings
The DXF/DWG user interface looks for the settings file dxfdwg.def in the local directory. If you find the settings file, its contents will be used for the initial settings of the user interface. If you do not find a local file, then the UGII_BASE_DIR\dxfdwg\dxfdwg.def file is used.
Import
Units
DWG files have unit information in them, as do AutoCAD 2000 DXF files. If Unit specification is available the system will use it regardless of this setting. However, earlier versions of DXF did not support a unit designation, so you use this setting to indicate the units of the DXF data.
Mapping Specifications
The Color mapping specification lets you identify a file where you have set up a mapping between the Unigraphics NX color numbers and the AutoCAD color numbers.
The Line Font mapping specification lets you identify a file where you have set up a mapping between Unigraphics NX line font names and AutoCAD line font names.
The Character Font mapping specifications lets you identify a file where you have set up a mapping between Unigraphics NX character font names and AutoCAD character font names.
See Mapping Specification File Processing for details on how to format these files to override the default settings.
Mapping Specification File Processing
The Unigraphics NX DXF/DWG translator provides the ability to specify how character fonts, line styles, and colors should be mapped when moving data between Unigraphics NX and AutoCAD.
You use the mapping specifications when you know that a particular font will present the data better in the receiving system. While Unigraphics NX provides a suite of AutoCAD fonts, you may be using your own Unigraphics NX fonts and/or you and your supplier may have agreed on a font that is not one of the standard fonts provided by Unigraphics NX.
Mapping files are simple ASCII files (the formats are described below), normally named with the <.txt> extension. However you can actually name them whatever you want.
The way mapping files are processed minimizes the amount of information you have to provide in them. Only the particular values you want to change need specification in the named mapping file. All other values use the standard mappings provided with the product.
Comments can be included in all mapping files by preceding them with an exclamation point (!). You can add white space to improve readability.

## Slide 8: DXF/DWG Translator
Charakterfont Mapping
Syntax: Dxfdwg.exe X:\InputDir\Input.prt X:\KonvertDir\Output.dxf Output.log DxfDwg_KonvertierungsSetup.def
DxfDwg_KonvertierungsSetup.def
...
... CHARACTERFONT_MAPPING_FILENAME=R:\NXExport\ClientScripts\dxfdwg_CHARACTERFONT_MAPPING_DataExpo.def
...
...
dxfdwg_CHARACTERFONT_MAPPING_DataExpo.def
! Font Mapping file for DxfDwg konversion
! creaded 05.12.2007 J.Fes
export : blockfont = isocp.shx, 1
export : blockvar = isocp.shx, 1
export : KBA-Symbolfont = isocp.shx, 1
export : barcode = isocp.shx, 0.8
export : din = isocp.shx, 0.8
export : dinbreit = isocp.shx, 1.1
export : dinschmal = isocp.shx, 0.7
export : greekfont = isocp.shx, 1
export : hausschrift = isocp.shx, 1
export : helvet = isocp.shx, 1
export : indexfont = isocp.shx, 1
export : iso8859_1 = isocp.shx, 0.8
export : kba_code39 = isocp.shx, 1
export : latin_extended = isocp.shx, 1
export : russian = isocp.shx, 1
Testnummer: 87674099/D

## Slide 9: Step Erzeugung
Informationen zum Export im Stepformat
Command line must be in the following format:
step214ug [D=<default file>.def] [M=<mode of operation>]
[O=<output file name>] [L=<log file name>] [<part file>]
(Brackets above refer to an optional argument)
How do the translators work with Teamcenter Engineering?
If you are running from inside of NX using the File→Export, you will have direct access to the Teamcenter Engineering file selection.
If you are importing, you need to do a File→Import to the Current part and then use the normal Save function to store the results in Teamcenter Engineering.
You cannot access Teamcenter Engineering files from the external user interface.
You can use the command line execution option to export a Teamcenter Engineering file. To do this you need to specify a particular input parameter. The example uses STEP 203 but STEP 214 and IGES behave similarly. DXF/DWG does not support exporting Teamcenter Engineering files from the command line.
Source your Teamcenter Engineering environment,
set PATH=%UGII_ROOT_DIR%;%PATH%
g:\ugnx40\STEP203UG\step203ug.exe -I="@DB000201/A D=g:\ugnx40\STEP203UG\step203ug.def
The path of step203ug.exe and step203.def will be unique for each environment. The above example translated UGMASTER 000201\a to STEP and saved the file as 000201_a.stp.
D:\UGS\UGNX4\STEP214UG
D:\UGS\UGNX4\STEP203UG
Beispiel für ein Export via cmd
""D:\UGS\UGNX4\step214ug\step214ug.cmd" "@DB/CountMe/A" o="C:\TEMP\000204_000\CountMe_A.stp" l="C:\TEMP\000204_000\CountMe_A.log" d="V:\JobManager\ProgEntw\Ver02\JobManagerV2\90-DATA\CustomerNameShort_SettingsGlobal\10-JobScripts\NXDataProcessIng\ClientScripts\step214ug.def" -pim=yes -u=infodba -p=infodba
Notes: "D:\UGS\UGNX4\step214ug\step214ug.exe" "@DB/CountMe/A" o="C:\TEMP\000204_000\CountMe_A.stp" l="C:\TEMP\000204_000\CountMe_A.log" d="V:\JobManager\ProgEntw\Ver02\JobManagerV2\90-DATA\CustomerNameShort_SettingsGlobal\10-JobScripts\NXDataProcessIng\ClientScripts\step214ug.def" -pim=yes -u=infodba -p=infodba

## Slide 10: Step Erzeugung

## Slide 11: # Hinweise zum Arbeiten mit Powerpoint Dokumentation
Bitte folgendes berücksichtigen !
# Standard Symbole