## Slide 1: Datenexport
#Lup: 02.01.2018 / J.Fes
Documentation Dataexchange with PLMJobManager

## Slide 2: Export Bedingungen
Übersicht welche wie werden die unterschiedlichen Datasettypen exporiert
Datasettype | Step Export | Parasolid Export | DXF Export | JTExport
Einzelteile (SP=Single Parts) |  |  |  | 
UGMASTER/SP | YES | YES | NO | 
UGALTREP/SP | YES | YES | NO | 
UGPART/SP | NO? | NO | YES | 
Baugruppen (AP=Assembly Parts) |  |  |  | 
UGMASTER/AP | YES | YES | NO | 
UGALTREP/Ap | YES | YES | NO | 
UGPART/Ap | NO? | NO | YES | 
Export Optionen:
  Mit welchen Refset Einstellungen soll exportiert werden  siehe load_options.def
  Was ist zu unterscheiden beim Export von SP Single Parts und AP Assembly Parts
  Wie sollen bei den Exports Rohteil und Fertigteil unterschieden werden Frage soll das Rohteil beim Export enthalten sein
  Export von Altreps
  Export DXF ..\dxfdwg_M.def wichtig:  enthält verweis auf
  Export DXF Fonts  ..\dxfdwg_CHARACTERFONT_MAPPING_DataExpo.def ..\dxfdwg_M.def wichtig:  enthält verweis aufdxfdwg_CHARACTERFONT_MAPPING_DataExpo.def

## Slide 3: Ugto2d.exe DXF Export Optionen für
Optionparameter for Ugto2D
$UGII_BASE_DIR/ugto2d/ugto2d [options]
You can give the options in any order. Each uses an option= format. Use spaces to delimit multiple options.
Valid options include:
[i=]<input part file name> | Mandatory
[o=<output part file name>] | Optional, default: <input part file name>_2d.prt
[l=<log file name>] | Optional, default: <input part file name>_2d.log
[d=<user-defined settings file>] | Optional, default: ugto2d.def
[a=<assembly options file>] | Optional, default: load_options.def
[m=<'output to' mode>] | Optional, default: m (for Modeling) Valid modes are: d (for Drafting) and m (for Modeling)
[draw=<choose drawing to translate>] | Optional, default: current drawing
[view=<choose view to translate>] | Optional, default: current view)
Tce | -pim=yes –u=TceUser –p=TcePasswort
You can run the command line in Teamcenter Engineering on Windows. The following example translates UGMASTER 000201/a into a 2D part file: 000201_a_2d.prt
1. Source your Teamcenter Engineering environment.
2. set PATH=%UGII_ROOT_DIR%;%PATH%
3. ugto2d.exe i=@DB000201/A
Input File Name
The i= label is optional when specifying the input part file name.
If there is no input file name given on the command line, you are asked for input data. See Example of Prompt - Mode Invocation of Translator.
You can supply input file name(s) through the settings file using the INPUT_PARTS_LIST keyword. You can control the input directory using the INPUT_PARTS_DIR keyword.

## Slide 4: Ugto2d Command Line/User-Defined Settings File Examples
Command: ugto2d onedrawing.prt AND ugto2d multidrawing.prt d=my.def
Settings: using all defaults
Yields: onedrawing_2d.prt AND multidrawing_2d.prt
Command: ugto2d twodrawings.prt d=my.def
Settings: DEFAULT_DRAWING_CNV = _ALL_
Yields: _twodrawings_sh1_2d.prt AND twodrawings_sh2_2d.prt
Command: ugto2d d=my.def
Settings:
INPUT_PARTS_DIR=d:\in\
OUTPUT_PARTS_DIR=f:\out\
INPUT_PARTS_LIST=one.prt, twodrawings.prt, three.prt
OUTPUT_PARTS_LIST=bob.prt, fred.prt, three.prt
Reads in: d:\in\one.prt, d:\in\twodrawings.prt, d:\in\three.prt
Writes out: f:\out\bob_2d.prt, f:\out\fred_sht1_2d.prt, f:\out\fred_sht2.prt, f:\out\three_2d.prt
Command: ugto2d multidrawing.prt d=my.def
Settings:
INPUT_PARTS_DIR=/in/
OUTPUT_PARTS_DIR=OUTPUT_TO_INPUT_DIR
DEFAULT_CNV_MODE = DRAFTING
DEFAULT_DRAWING_CNV = CURRENT
ASSEM_OPTIONS=/asm/missingcompok/load_options.def
Reads in: /in/multidrawing.prt
Writes out: /in/multidrawing_2d.prt with results in drafting rather than in modeling. Only the current drawing is processed, rather than processing _ALL_ drawings. The provided options file governs assembly loading behaviors. This could be supplied via the a=/asm/missingcompok/load_options.def command line option.
Command: ugto2d multi.prt d=my.def
Settings:
INPUT_PARTS_DIR=d:\in\
OUTPUT_PARTS_DIR=OUTPUT_TO_CURR_DIR
Reads: d:\in\multi.prt
Writes (given current directory is m:\test\fri\batch\):
m:\test\fri\batch\multi_sh1_2d.prt
m:\test\fri\batch\multi_sh2_2d.prt

## Slide 5: DXF/DWG Translator
Settings
The DXF/DWG user interface looks for the settings file dxfdwg.def in the local directory. If you find the settings file, its contents will be used for the initial settings of the user interface. If you do not find a local file, then the UGII_BASE_DIR\dxfdwg\dxfdwg.def file is used.
Import
Units
DWG files have unit information in them, as do AutoCAD 2000 DXF files. If Unit specification is available the system will use it regardless of this setting. However, earlier versions of DXF did not support a unit designation, so you use this setting to indicate the units of the DXF data.
Mapping Specifications
The Color mapping specification lets you identify a file where you have set up a mapping between the Unigraphics NX color numbers and the AutoCAD color numbers.
The Line Font mapping specification lets you identify a file where you have set up a mapping between Unigraphics NX line font names and AutoCAD line font names.
The Character Font mapping specifications lets you identify a file where you have set up a mapping between Unigraphics NX character font names and AutoCAD character font names.
See Mapping Specification File Processing for details on how to format these files to override the default settings.
Mapping Specification File Processing
The Unigraphics NX DXF/DWG translator provides the ability to specify how character fonts, line styles, and colors should be mapped when moving data between Unigraphics NX and AutoCAD.
You use the mapping specifications when you know that a particular font will present the data better in the receiving system. While Unigraphics NX provides a suite of AutoCAD fonts, you may be using your own Unigraphics NX fonts and/or you and your supplier may have agreed on a font that is not one of the standard fonts provided by Unigraphics NX.
Mapping files are simple ASCII files (the formats are described below), normally named with the <.txt> extension. However you can actually name them whatever you want.
The way mapping files are processed minimizes the amount of information you have to provide in them. Only the particular values you want to change need specification in the named mapping file. All other values use the standard mappings provided with the product.
Comments can be included in all mapping files by preceding them with an exclamation point (!). You can add white space to improve readability.

## Slide 6: DXF/DWG Translator
Charakterfont Mapping
Syntax: Dxfdwg.exe X:\InputDir\Input.prt X:\KonvertDir\Output.dxf Output.log DxfDwg_KonvertierungsSetup.def
DxfDwg_KonvertierungsSetup.def
...
... CHARACTERFONT_MAPPING_FILENAME=R:\NXExport\ClientScripts\dxfdwg_CHARACTERFONT_MAPPING_DataExpo.def
...
...
dxfdwg_CHARACTERFONT_MAPPING_DataExpo.def
! Font Mapping file for DxfDwg konversion
! creaded 05.12.2007 J.Fes
export : blockfont = isocp.shx, 1
export : blockvar = isocp.shx, 1
export : KBA-Symbolfont = isocp.shx, 1
export : barcode = isocp.shx, 0.8
export : din = isocp.shx, 0.8
export : dinbreit = isocp.shx, 1.1
export : dinschmal = isocp.shx, 0.7
export : greekfont = isocp.shx, 1
export : hausschrift = isocp.shx, 1
export : helvet = isocp.shx, 1
export : indexfont = isocp.shx, 1
export : iso8859_1 = isocp.shx, 0.8
export : kba_code39 = isocp.shx, 1
export : latin_extended = isocp.shx, 1
export : russian = isocp.shx, 1
Testnummer: 87674099/D

## Slide 7: Step Erzeugung
Informationen zum Export im Stepformat
Command line must be in the following format:
step214ug [D=<default file>.def] [M=<mode of operation>]
[O=<output file name>] [L=<log file name>] [<part file>]
(Brackets above refer to an optional argument)
How do the translators work with Teamcenter Engineering?
If you are running from inside of NX using the File→Export, you will have direct access to the Teamcenter Engineering file selection.
If you are importing, you need to do a File→Import to the Current part and then use the normal Save function to store the results in Teamcenter Engineering.
You cannot access Teamcenter Engineering files from the external user interface.
You can use the command line execution option to export a Teamcenter Engineering file. To do this you need to specify a particular input parameter. The example uses STEP 203 but STEP 214 and IGES behave similarly. DXF/DWG does not support exporting Teamcenter Engineering files from the command line.
Source your Teamcenter Engineering environment,
set PATH=%UGII_ROOT_DIR%;%PATH%
g:\ugnx40\STEP203UG\step203ug.exe -I="@DB000201/A D=g:\ugnx40\STEP203UG\step203ug.def
The path of step203ug.exe and step203.def will be unique for each environment. The above example translated UGMASTER 000201\a to STEP and saved the file as 000201_a.stp.
D:\UGS\UGNX4\STEP214UG
D:\UGS\UGNX4\STEP203UG
Beispiel für ein Export via cmd
""D:\UGS\UGNX4\step214ug\step214ug.cmd" "@DB/CountMe/A" o="C:\TEMP\000204_000\CountMe_A.stp" l="C:\TEMP\000204_000\CountMe_A.log" d="V:\JobManager\ProgEntw\Ver02\JobManagerV2\90-DATA\CustomerNameShort_SettingsGlobal\10-JobScripts\NXDataProcessIng\ClientScripts\step214ug.def" -pim=yes -u=infodba -p=infodba
Notes: "D:\UGS\UGNX4\step214ug\step214ug.exe" "@DB/CountMe/A" o="C:\TEMP\000204_000\CountMe_A.stp" l="C:\TEMP\000204_000\CountMe_A.log" d="V:\JobManager\ProgEntw\Ver02\JobManagerV2\90-DATA\CustomerNameShort_SettingsGlobal\10-JobScripts\NXDataProcessIng\ClientScripts\step214ug.def" -pim=yes -u=infodba -p=infodba

## Slide 8: Step Erzeugung
Settings

## Slide 9: Step Import step203ug.exe
Command line must be in the following format:
step203ug [D=<default file>.def] [M=<mode of operation>]
[O=<output file name>] [L=<log file name>] [<part file>]
(Brackets above refer to an optional argument)
"C:\Program Files\Siemens\NX10\step203ug\step203ug.exe" d="C:\NX_Custom\NX100_UGII_TMP_DIR\jopp488462A101et.def“
AP203_COLLAY_EXT =Off
ASSEMBLY_MAP = Off
AUTOMATIC_SURF_SEW = Off
Author =
Authorization =
CHOOSE_DIRECTION =STEP to UG
CNV_MODE =On-Line
DSP_MASK =Fatal,Severe,Error,Warning,Information,Status,Summary,Prefix
Description =
EXPORT_EXTERNAL_REFERENCES =Off
EXPORT_EXTERNAL_REFERENCE_FORMAT =STEP
EXPORT_VALPROPS =Off
FILE_FILTER =V:\CustomersDataL\KBA.Iberica\2018-01-02-ExampleData\ImportTest\*.stp
File_Name =
INDIVIDUAL_LIST =V:\CustomersDataL\KBA.Iberica\2018-01-02-ExampleData\ExportTest3\008043000a_asm.prt
Imp_Level =1
LOG_FILE =V:\CustomersDataL\KBA.Iberica\2018-01-02-ExampleData\ExportTest3\008043000a_asm.log
MODULES_MASK =Wireframe,Surfaces,Solids,PMI
MSG_MASK =Fatal,Severe,Error,Warning,Information,Status,Summary,Prefix
Organization =
PA_EDGE_FACE_BSPLINE_APPROX_TOL =0.0254
PROCESS_PART_LIST =V:\CustomersDataL\KBA.Iberica\2018-01-02-ExampleData\ImportTest\008043000a_asm.stp
PROCESS_PART_LIST = #PROCESS_PART_LIST#
Pre_Version =STEP203UG NX 10.0
RECALL_DEF_FILE =step203ug.def
SAVE_DEF_FILE =step203ug.def
SHORT_LONG_NAMES =Long
SMOOTH_BSURFS = On
UGI_COMP_FAIL =Abort if Load Fails
UGI_COMP_SUB =Do not Allow Substitution
UGI_LAYERD_MASK =
UGI_LAYERE_MASK =
UGI_LAYER_MASK =1-256
UGI_LOAD_COMP =Load Components
UGI_LOAD_OPTION =Load From Assem Dir
UGI_LOAD_VER =Load Exact Version
UGI_PROC_ASSEM =Use load_options.def options
UGI_SEARCH_DIRS =
ZERO_LAYER_DEFAULT = 1

## Slide 10: Step Import step203ug.exe
"C:\Program Files\Siemens\NX10\step203ug\step203ug.exe" d="C:\NX_Custom\NX100_UGII_TMP_DIR\jopp488462A101et.def“
AP203_COLLAY_EXT =Off
ASSEMBLY_MAP = Off
AUTOMATIC_SURF_SEW = Off
Author =
Authorization =
CHOOSE_DIRECTION =STEP to UG
CNV_MODE =On-Line
DSP_MASK =Fatal,Severe,Error,Warning,Information,Status,Summary,Prefix
Description =
EXPORT_EXTERNAL_REFERENCES =Off
EXPORT_EXTERNAL_REFERENCE_FORMAT =STEP
EXPORT_VALPROPS =Off
FILE_FILTER =V:\CustomersDataL\KBA.Iberica\2018-01-02-ExampleData\ImportTest\*.stp
File_Name =
INDIVIDUAL_LIST =V:\CustomersDataL\KBA.Iberica\2018-01-02-ExampleData\ExportTest3\008043000a_asm.prt
Imp_Level =1
LOG_FILE =V:\CustomersDataL\KBA.Iberica\2018-01-02-ExampleData\ExportTest3\008043000a_asm.log
MODULES_MASK =Wireframe,Surfaces,Solids,PMI
MSG_MASK =Fatal,Severe,Error,Warning,Information,Status,Summary,Prefix
Organization =
PA_EDGE_FACE_BSPLINE_APPROX_TOL =0.0254
PROCESS_PART_LIST =V:\CustomersDataL\KBA.Iberica\2018-01-02-ExampleData\ImportTest\008043000a_asm.stp
Pre_Version =STEP203UG NX 10.0
RECALL_DEF_FILE =step203ug.def
SAVE_DEF_FILE =step203ug.def
SHORT_LONG_NAMES =Long
SMOOTH_BSURFS = On
UGI_COMP_FAIL =Abort if Load Fails
UGI_COMP_SUB =Do not Allow Substitution
UGI_LAYERD_MASK =
UGI_LAYERE_MASK =
UGI_LAYER_MASK =1-256
UGI_LOAD_COMP =Load Components
UGI_LOAD_OPTION =Load From Assem Dir
UGI_LOAD_VER =Load Exact Version
UGI_PROC_ASSEM =Use load_options.def options
UGI_SEARCH_DIRS =
ZERO_LAYER_DEFAULT = 1

## Slide 11: Step Import step203ug.exe
"C:\Program Files\Siemens\NX10\step203ug\step203ug.exe" d="C:\NX_Custom\NX100_UGII_TMP_DIR\jopp488462A101et.def“
http://ww3.cad.de/foren/ubb/Forum4/HTML/010083.shtml
Zitat:
Original erstellt von Majomouse:
Guten Morgen,
auf Anfrage bei Siemens habe ich eine Liste erhalten bezüglich der Optionen im Settings-File (Import und Export Step 203 und Step 214). Darin sind gefühlte 100 Keywords enthalten.
Die klare Auflistung mit kurzer Beschreibung über die entsprechenden Auswirkungen und Abhängigkeiten der einzelnen Keywords ist in folgende Topics eingeteilt:
TRANSLATION CONTROL OPTIONS
IMPORT OPTIONS
EXPORT OPTIONS
OPTIONAL IMPORT KEYWORDS
OPTIONAL EXPORT KEYWORDS
RESERVED KEYWORDS
Für mich beinhaltet diese Liste genau das, wonach ich gesucht habe. Da ich nicht sicher bin, ob ich diese Liste hier bedenkenlos veröffentlichen kann, lasse ich es lieber bleiben.
Ihr wisst ja wie Ihr mich erreichen könnt...
Beste Grüße, danke für Eure Hilfe...
...ein schönes Wochenende...
Stefan

## Slide 12: Step Import step203ug.exe
Step203.def
Notes: http://download.plmjobmanager.com/Screenshots/ScreenShot_[2018-01-25_16-52-44]_[jopp].jpg

## Slide 13: Util step203ug.exe
Online Documentation: docs.plm.automation.siemens.com
https://docs.plm.automation.siemens.com/tdoc/nx/10.0.3/nx_help#uid:index_xid458198
https://docs.plm.automation.siemens.com/tdoc/nx/10.0.3/nx_help#uid:index_xid458198:xid454879
https://docs.plm.automation.siemens.com/tdoc/nx/10.0.3/nx_help#uid:index_xid458198:xid454880
https://ww3.cad.de/foren/ubb/uploads/Majomouse/Solution_Center.txt
 Some Details Regarding Options

## Slide 14: Util step203ug.exe
Online Documentation: docs.plm.automation.siemens.com
https://docs.plm.automation.siemens.com/tdoc/nx/10.0.3/nx_help#uid:index_dataexchange:xid461636
Keywords | Values
UGI_PROC_ASSEM | Overwrite load_options.def values
UGI_COMP_FAIL | Abort if Load Fails or Continue if Load Fails
UGI_COMP_SUB | Allow Substitution or Do not Allow Substitution
UGI_LOAD_COMP | Do Not Load Comps or Load Components
UGI_LOAD_VER | Load Exact Version or Load Latest Version
UGI_SEARCH_DIRS | D:\workdir,d:\parts\testdata,c:\testdata
Notes: UGI_COMP_FAIL =Abort if Load Fails
UGI_COMP_SUB =Do not Allow Substitution
UGI_LAYERD_MASK =
UGI_LAYERE_MASK =
UGI_LAYER_MASK =1-256
UGI_LOAD_COMP =Load Components
UGI_LOAD_OPTION =Load From Assem Dir
UGI_LOAD_VER =Load Exact Version
UGI_PROC_ASSEM =Use load_options.def options
UGI_SEARCH_DIRS =
ZERO_LAYER_DEFAULT = 1

## Slide 15: UG*.exe
ug_ps_convert.exe -h
ugnx_cad2prt.exe -h
ug_convert_part.exe -h

## Slide 16: ug_edit_part_names
Utility to rename the partfile inside and the filename in example:
ug_edit_part_names C:\addPLM\CustomersDataL\KBA.Iberica\ExcangeFolder\92-RenameTest\432500252_prt.prt
–o C:\addPLM\CustomersDataL\KBA.Iberica\ExcangeFolder\92-RenameTest\432500252.prt
-change_name 432500252_prt.prt 432500252.prt

## Slide 17: Util UG_Clone.exe
Online Documentation: docs.plm.automation.siemens.com
https://docs.plm.automation.siemens.com/tdoc/nx/10/nx_help#uid:imexport_clone_impexp_clone_run
https://docs.plm.automation.siemens.com/tdoc/nx/10/nx_help#uid:index_tcint:id1299690:id1299704:clone_clone_log_files1
..\NXImport\ug_clone_SPLM-Documentation.pdf

## Slide 18: Util  ugpc.exe
Help
D:\NXDataNX000>"C:\Program Files\Siemens\NX12\NXBIN\ugpc.exe" -help
UGPC Help: ugpc takes the following arguments:
<part1> <part2>
This argument specifies one or more part filenames to produce a listing
for. This is the only ugpc argument that is not optional.
-n
This optional argument indicates that ugpc should print the number
of components found at a given level.
-s
This optional argument indicates that ugpc should print an indented listing
of the assembly structure. If a number is specified immdediately after
the -s (e.g -s4) you can control the amount of the indentation,
-p<directory1> -p<directory2>
This optional argument provides a way to specify one or more directories
for ugpc to search for components in. The directory must be specified
immediately after the -p without a space (e.g -p/parts/released)
-a
This optional argument specifies that the assembly should be reported
`as saved'. By default, ugpc will attempt to search for components in
directories where the top-level assembly or its components have previously
been found. If this option is used, ugpc will not attempt to do this.

## Slide 19: Einstellungen JobManager
Einstellungen Scripts/Param

## Slide 20: Einstellungen JobManager
Einstellungen Job Control